## Slide 1: Pregnancy Diagnosis
Using Real Time Ultrasound (RTU)

## Slide 2: Pregnancy Failure 20-30% of mated sows fail to farrow
Koketsu et al., 1997, Theriogenology

## Slide 3: Performing RTU
A gel is used on probe to ensure good contact with skin
Probe is placed on sow’s flank (either side)
Probe is directed at uterine horn

## Slide 4: How RTU works
Sound waves are transmitted and received by the probe as they reflect off tissues.
Liquids absorb the waves and are displayed as Black.
Tissues reflect most of the waves and are displayed as White.White

## Slide 5
Open
Pregnant
Examples

## Slide 6: Open
“Fluffy cloud” appearance
Bright white line is present (intestinal, rectal or uterine wall)
No fluid filled vesicles present

## Slide 7: Pregnant
Round, black, fluid filled vesicles are present
More than one fluid filled vesicle (One may represent the bladder)
No bright white line
No “Fluffy cloud” appearance

## Slide 8: Day 21
Vesicles may or may not be detected at this stage

## Slide 9: Day 23
Vesicles are just becoming developed enough for RTU detection

## Slide 10: Day 25
Black, fluid filled vesicles are easily detected at this stage

## Slide 11: What Influences RTU? -Fluid Diameter
Koketsu et al., 1997, Theriogenology

## Slide 12: Optimal Times for RTU -Time to Decide on a Pregnancy Diagnosis and Fluid Diameter
Koketsu et al., 1997, Theriogenology

## Slide 13: Day 35
Bone mineralization starts to occur
Vesicle fluid starts to decrease

## Slide 14: Day 40
Loss of vesicle fluid makes pregnancy detection more difficult.

## Slide 15: Day 44
Fetuses
Most accurate pregnancy detection is performed between days 25-35

## Slide 16: Day 50
Fetal development leads to detection of fetal organs
May be difficult to differentiate sow organs from fetal organs.

## Slide 17: Day 74
Fetal ribs and other bones

## Slide 18: Potential Advantages for using RTU
Identify open females for rebreed or cull
Minimize non-productive sow days
Prevent unintended culling of pregnant sows
Identify the extent and timing of pregnancy failure

## Slide 19: Potential Drawbacks for using RTU
Animal sensitivity to abdominal touch
  Irritated animals can injure person and equipment
Cost of purchasing a RTU machine
  Cost range approximately $3,500-$5,000 for farm use